## Slide 1
B.TECH PROJECT PRESENTATION
AXI4 Master with Burst Transfer
Support for DMA-to-Memory Data Movement
Electronics and Communication Engineering
Presented by: Yelleti Harshavardhan
Roll No.: 2400040454
KL University | Academic Year 2025–2026
Project Guide: Dr. M. Lakshmana Kumar
AXI4 MASTER WITH BURST TRANSFER SUPPORT
1

## Slide 2
Abstract
PROJECT OVERVIEW
AXI4 MASTER WITH BURST TRANSFER SUPPORT
2
This project implements and verifies a modular AXI4 Master for DMA-based memory-to-memory data movement. Burst calculation, independent read/write engines, FIFO buffering, and transaction tracking are combined to transfer data with reduced address-phase overhead.
Interface
32-bit address bus
64-bit data bus
Burst configuration
Up to 16 beats per burst
8 bytes per beat = 128 bytes
Verification
256-byte transfer
4 KB boundary test
Simulation reported “ALL TESTS PASSED.” Synthesis and implementation reports were generated in Vivado 2025.2.

## Slide 3
Problem Statement and Objectives
MOTIVATION
AXI4 MASTER WITH BURST TRANSFER SUPPORT
3
Problem
Single-beat transfers require repeated address transactions. A DMA master must coordinate burst length, handshakes, buffering, responses, and 4 KB boundary restrictions.
Objective
Design a modular AXI4 master that moves data between memory addresses, generates valid bursts, handles read/write sequencing, and verifies data integrity.
Key design goals
Support AXI4 read and write burst transactions.
Limit bursts by remaining bytes, FIFO capacity, maximum length, and 4 KB boundary.
Verify data movement and completion through a self-checking testbench.

## Slide 4
AXI4 Protocol Essentials
BACKGROUND
AXI4 MASTER WITH BURST TRANSFER SUPPORT
4
AW — Write Address
Write destination address and burst attributes.
W — Write Data
Write data beats; WLAST marks the final beat.
B — Write Response
Slave returns write completion status.
AR — Read Address
Read source address and burst attributes.
R — Read Data
Slave returns data; RLAST marks final beat.
A transfer occurs when VALID and READY are both high in the same clock cycle.

## Slide 5
System Architecture
DESIGN METHODOLOGY
AXI4 MASTER WITH BURST TRANSFER SUPPORT
5
DMA Controller
Transfer control
Burst Calculator
Length + 4 KB check
AXI4 Read Engine
AR / R channels
FIFO
Data buffer
AXI4 Write Engine
AW / W / B
Outstanding Tracker
Tracks issued and completed work.
AXI4 RAM Slave
Internal memory model for verification.
Data path: Source memory → Read engine → FIFO → Write engine → Destination memory

## Slide 6
Design Parameters and Configuration
RTL IMPLEMENTATION
AXI4 MASTER WITH BURST TRANSFER SUPPORT
6
Parameter | Configured value
Address width | 32 bits
Data width | 64 bits
ID width | 4 bits
FIFO depth parameter | 512
Maximum burst length | 16 beats
Bytes per beat | 8 bytes
Maximum data per burst | 128 bytes
Tool / RTL | Vivado 2025.2 / SystemVerilog RTL

## Slide 7
Burst Calculation and 4 KB Boundary
KEY DESIGN LOGIC
AXI4 MASTER WITH BURST TRANSFER SUPPORT
7
Selected burst length is limited by the most restrictive condition:
B = min(B_remaining, B_boundary, C_FIFO, MAX_BURST)
Bytes per beat = 64 / 8 = 8 bytes.
Maximum burst = 16 × 8 = 128 bytes.
Bytes to 4 KB boundary = 4096 − (address mod 4096).
AXI4 encodes burst length as beats − 1: ARLEN = B − 1 and AWLEN = B − 1.
After a burst: next address = address + (B × 8); remaining bytes decrease by B × 8.

## Slide 8
Pseudocode: Burst-Length Calculation
ALGORITHM 1 · BOUNDARY-AWARE BURST SELECTION
INPUT: current_address, remaining_bytes, fifo_free_beats
CONSTANTS: BYTES_PER_BEAT = 8, MAX_BURST = 16, BOUNDARY = 4096
bytes_to_boundary = BOUNDARY - (current_address MOD BOUNDARY)
beats_remaining = remaining_bytes DIV BYTES_PER_BEAT
beats_to_boundary = bytes_to_boundary DIV BYTES_PER_BEAT
burst_beats = MIN(beats_remaining,
beats_to_boundary,
fifo_free_beats,
MAX_BURST)
IF burst_beats > 0:
AXI_ARLEN = burst_beats - 1 // read burst
AXI_AWLEN = burst_beats - 1 // write burst
ELSE:
WAIT until transfer/FIFO conditions permit progress
The pseudocode summarizes the burst-selection equations used in the report; it is not synthesizable RTL.
AXI4 MASTER WITH BURST TRANSFER SUPPORT
8

## Slide 9
Pseudocode: DMA Transfer Control
ALGORITHM 2 · READ, BUFFER, WRITE, AND UPDATE
ON start_request:
source_address = configured_source
destination_address = configured_destination
remaining_bytes = configured_length
busy = 1
done = 0
WHILE remaining_bytes > 0:
read_beats = calculate_burst(source_address, remaining_bytes, fifo_space)
issue AXI read address and receive read data into FIFO
wait until the required read data is available
write_beats = calculate_burst(destination_address, remaining_bytes, fifo_data)
issue AXI write address and send FIFO data
assert WLAST on the final beat of the write burst
wait for the AXI write response
bytes_done = completed_beats * BYTES_PER_BEAT
source_address += bytes_done
destination_address += bytes_done
remaining_bytes -= bytes_done
busy = 0
done = 1
only. Exact read/write overlap and counter updates depend on the implemented RTL state machines.
AXI4 MASTER WITH BURST TRANSFER SUPPORT
9

## Slide 10
Functional Verification
SIMULATION RESULTS
AXI4 MASTER WITH BURST TRANSFER SUPPORT
10
Test Case 1 — 256-byte transfer
Source memory initialized with known data. After DMA completion, destination contents were compared with source data.
Result: PASS
Test Case 2 — 4 KB boundary
Transfer begins at 0x0FE0 near the 0x1000 boundary. Burst splitting prevents an individual burst from crossing the boundary.
Result: PASS
Overall simulation result: ALL TESTS PASSED
These results apply to the tested RTL and internal AXI4 RAM verification setup; they do not by themselves prove external DDR or physical-board functionality.

## Slide 11
Simulation Waveform and Transfer Sequence
VERIFICATION EVIDENCE
AXI4 MASTER WITH BURST TRANSFER SUPPORT
11
1
Start request
2
Read address handshake
3
Read data → FIFO
4
Write address/data
5
Write response
6
Done asserted
Use the project’s actual XSim waveform screenshot on this slide if a visual waveform is required.

## Slide 12
FPGA Resource Utilization and Timing
IMPLEMENTATION RESULTS
AXI4 MASTER WITH BURST TRANSFER SUPPORT
12
Slice LUTs
285 used | 0.45%
Slice Registers
158 used | 0.12%
Bonded I/O
62 used | 29.52%
Timing metric | Reported result
Clock frequency | 100 MHz
Synthesis WNS | +1.594 ns
Post-implementation WNS | +0.981 ns
Post-implementation TNS | 0 ns
Post-implementation WHS | +0.122 ns
THS / failing endpoints | 0 ns / 0

## Slide 13
Power Analysis
VIVADO POWER ESTIMATE
AXI4 MASTER WITH BURST TRANSFER SUPPORT
13
Total on-chip power
0.219 W
Dynamic power
0.111 W
Device static power
0.108 W
Estimated junction temperature: 27.5 °C
Ambient assumption: 25 °C
Process: Typical
Power values are tool estimates; actual board power can vary.
Figure: Vivado on-chip power analysis

## Slide 14
Post-Implementation Timing Summary
TIMING CLOSURE
AXI4 MASTER WITH BURST TRANSFER SUPPORT
14
Reported: WNS +0.981 ns, TNS 0 ns, WHS +0.122 ns, THS 0 ns, and zero failing setup/hold endpoints. Vivado reports that user-specified timing constraints are met for this run.
Timing closure is constraint-dependent; CDC behavior should also be validated.

## Slide 15
Implementation and Bitstream Status
VIVADO RUN EVIDENCE
AXI4 MASTER WITH BURST TRANSFER SUPPORT
15
The screenshot captured impl_1 while write_bitstream was running. Confirm that the run finishes successfully before reporting the bitstream as generated or claiming successful FPGA programming.

## Slide 16
Conclusion and Future Scope
SUMMARY
AXI4 MASTER WITH BURST TRANSFER SUPPORT
16
Conclusion
A modular AXI4 DMA master was designed and functionally verified for the reported test cases. The design includes burst calculation, read/write engines, FIFO buffering, transaction tracking, and 4 KB boundary handling.
Future Scope
Integrate external DDR/MIG, expand verification for backpressure and error responses, test larger transfers, improve transaction scheduling, and validate the design on the target FPGA board.
Key result: 256-byte transfer PASS • 4 KB boundary test PASS • Implementation timing summary has zero failing endpoints
Thank you